## Slide 1
Enrico Ubaldino

## Slide 2: What’s?
Questa SIM is a verification and simulation tool for VHDL, Verilog, SystemVerilog, SystemC, and mixed-language designs. By default, Questa SIM optimizations are automatically performed on all designs.
Questa SIM Code Coverage gives you graphical and report file feedback on which executable statements, branches, conditions, and expressions in your source code have been executed.
Enrico Ubaldino

## Slide 3: Example Fulladder
Enrico Ubaldino

## Slide 4: VHDL Code FUlladder
Library IEEE;
Use IEEE.std_logic_1164.all;
Entity FullAdder is
Port (
A, B, Cin : in std_logic;
S, Cout : out std_logic );
End FullAdder;
Architecture bev of FullAdder is
begin
S <= A xor B xor Cin;
Cout <= (A and B) or ((A xor B) and Cin);
--Cout <= (A nand B) nand (C nand (A xor B)); --DeMorgan
End bev;
Enrico Ubaldino

## Slide 5: New project
File/New ->Project
Enrico Ubaldino

## Slide 6: Load sources file

## Slide 7: Compile all
vcom –work «file.vhd» for VHDL sources

## Slide 8: optimize
vopt +acc «name testbench» –o «name testbench opt»
Enrico Ubaldino

## Slide 9: Simulation & Add wave
vsim «name testbench opt»

## Slide 10: Tb waveform
run 600 ns
Enrico Ubaldino

## Slide 11: Coverage typeS
Enrico Ubaldino

## Slide 12: Coverage
vopt +cover=bcesxf «name test» –o «name test opt for cov»
vsim –coverage «name test opt for cov»
Enrico Ubaldino

## Slide 13: Code coverage icons
Enrico Ubaldino

## Slide 14: Code coverage 100%
run 1 ms or you can force signal state with wave editor or by command e.g
force SW 2#01000001 2# binary radix
Enrico Ubaldino

## Slide 15: Html coverage report
Tools/Coverage Report -> HTML
Enrico Ubaldino

## Slide 16: Ucdb coverage report
coverage save name.ucdb
A database developed by Mentor Graphics for capture of code coverage, functional coverage, and other metrics together in one place for post-regression analysis and reporting. Forms the basis of the UCIS industry standard in development in Accellera.
Enrico Ubaldino

## Slide 17: What is an Assertion?
Enrico Ubaldino

## Slide 18: Schematic
vsim –debugDB «testbench» then click on View/Schematic
Enrico Ubaldino

## Slide 19: Close simulation
Quit –sim or Simulate/ End simulation
Enrico Ubaldino

## Slide 20: Power analisys
Vcd2wlf file1.vcd file2.wlf open file .wlf
power add nsg_noctrl_tb/DUT/*
run 500us
power report -all -bsaif powerNSG.saif
vcd file powerNSG.vcd
vcd add nsg_noctrl_tb/DUT/*
coverage report -output reportpower.txt -srcfile=* -detail -all -annotate -assert -directive -cvg -pa -code t
Enrico Ubaldino

## Slide 21: Power analisys
I recommend monitoring internal signals
power add -ports -internal -r nsg_noctrl_tb/DUT/linexp_gen/* START REG
power report -all -bsaif power_analysis_NSG_SG_linexp.saif STOP REG
Enrico Ubaldino